Dequantize
Dequantize // Maps quantized input to real output
# Description
Produces a tensor of element type type and the same shape as input where the value of each coordinate of output is the corresponding coordinate of input minus zero_point quantity multiplied by scale. The coordinate of scale and zero_point is the coordinate of output projected onto axes.
## Inputs
Name	Element Type	Shape
input	Any quantized type	Any
scale	Same as output	input shape projected onto axes
zero_point	Same as input	input shape projected onto axes

## Attributes
Name	Description
type	output element type; any real type
axes	Axis positions on which scale and zero_point are specified

## Outputs
Name	Element Type	Shape
output	type	Same as input

# Mathematical Definition

# C++ Interface
ngraph::op::Dequantize