MaxPool
MaxPool // MaxPool operations
# Description
Batched max pooling operation, with optional padding and window stride.
## Inputs
Name	Element Type	Shape
arg	any

## Attributes
Name	Description
window_shape	The window shape.
window_movement_strides	The window movement strides. (defaults to 1s)
padding_below	The below-padding shape. (defaults to 0s)
padding_above	The above-padding shape. (defaults to 0s)

## Outputs
Name	Element Type	Shape
output	same as arg

The input for max pooling is a data batch tensor of shape where , every , and where is the batch size, and is the number of channels (sometimes called features). The dimensions correspond to the shape of an -dimensional data item in a batch. For example, where , the data may represent a two-dimensional image. It also has two attributes:
1. the window shape a size vector where every ; and
2. the window movement strides, optional a vector of positive integers .
The output has the shape , where .
# Mathematical Definition
Given an input data batch tensor , the output tensor is defined by the equation

max{j_1 = s_1 i_1, dots, j_n = s_n i_n}^{j_1 = s_1 i_1 + w_1 - 1, dots, j_n = s_n i_n + w_n - 1} (T{in}[a,c,j_1,dots,j_n])
# C++ Interface
ngraph::op::v0::MaxPool