Quantize
Quantize // Maps real input to quantized output
# Description
Produces a tensor of element type type and the same shape as input where the value of each coordinate of output is the corresponding coordinate of input divided by scale rounded as specified by round_mode plus zero_point. The coordinate of scale and zero_point is the coordinate of output projected onto axes.
## Inputs
Name	Element Type	Shape
input	Any real type	Any
scale	Same as input	input shape projected onto axes
zero_point	Same as output	input shape projected onto axes

## Attributes
Name	Description
type	output element type; any quantized type
axes	Axis positions on which scale and zero_point are specified
round_mode	ROUND_NEAREST_TOWARD_INFINITY: round to nearest integer in case of two equidistant integers round away from zero e.g. 2.5 -> 3 -3.5 -> -4 / ROUND_NEAREST_TOWARD_ZERO: round to nearest integer in case of two equidistant integers round toward zero e.g. 2.5 -> 2 -3.5 to -3 / ROUND_NEAREST_UPWARD: round to nearest integer in case of two equidistant integers round up e.g. 2.5 to 3 -3.5 to -3 / ROUND_NEAREST_DOWNWARD: round to nearest integer in case of two equidistant integers round down e.g. 2.5 to 2 -3.5 to -4 / ROUND_NEAREST_TOWARD_EVEN: round to nearest integer in case of two equidistant integers round to even e.g. 2.5 to 2 -3.5 to -4 / ROUND_TOWARD_INFINITY: round to nearest integer away from zero / ROUND_TOWARD_ZERO: round to nearest integer toward zero / ROUND_UP: round to nearest integer toward infinity (ceiling) / ROUND_DOWN: round to nearest integer toward negative infinity (floor)

## Outputs
Name	Element Type	Shape
output	type	Same as input

# Mathematical Definition

# C++ Interface
ngraph::op::v0::Quantize